## Slide 1: MGB210 MONITORING AND MANAGING OPERATIONAL PEREFORMANCE
Topic 12 Lean Systems
Chapters 16
Russell, Roberta S., and Taylor III, Bernard W. (2017) Operations management: Creating value along the supply chain, 9th ed., Hoboken: NJ.
Chapters 14:
Stevenson, W.J. (2021) 14th ed. Operations Management, McGraw Hill, New York, NY.

## Slide 2: Lecture Outline
Lean Production and JIT (Definition)
Basic elements of Lean Production
Benefits of Lean Production
Implementing Lean Production
Lean Services
Leaning the Supply Chain
Lean Six Sigma

## Slide 3
Lean production – defined:
  An integrated management system that emphasizes the elimination of waste and the continuous improvement of operations (Russell and Taylor, 2014, p.723)
  A flexible system that uses minimal resources and produced high quality goods and services (Stevenson, 2021, p.612)
  Just in time (JIT) – smoothing the flow of material to arrive just as it is needed (Russell and Taylor, 2014, p.723).
  Eg Zara

## Slide 4: Lean System Principles
Five principles embody the way lean systems function:
  Identify customer values
  Focus on processes that create value
  Eliminate waste to create “flow”
  Produce only according to customer demand
  Strive for perfection
  Copyright ©2021 McGraw-Hill Education. All rights reserved. No reproduction or distribution without the prior written consent of McGraw-Hill Education.
14-4

## Slide 5: Benefits & Risks of Lean Systems
Key benefits
  Reduced waste
  Lower costs
  Increased quality
  Reduced cycle time
  Increased flexibility
  Increased productivity
Critical risks
  Increased stress on workers
  Fewer resources available if problems occur
  Supply chain disruptions can halt operations
  Copyright ©2021 McGraw-Hill Education. All rights reserved. No reproduction or distribution without the prior written consent of McGraw-Hill Education.
14-5

## Slide 6: Lean Operations: The Beginning
Lean operations began as lean manufacturing, also known as JIT, in the mid-1900s
Developed by Taiichi Ohno and Shigeo Ohno of Toyota
  Focus was on eliminating all waste from every aspect of the process
    Waste is viewed as anything that interferes with, or does not add value to, the process of producing automobiles
  Many terms used by Toyota, such as Kanban, Kaizen, and Muda, are commonly used industry wide.
  Copyright ©2021 McGraw-Hill Education. All rights reserved. No reproduction or distribution without the prior written consent of McGraw-Hill Education.
14-6

## Slide 7: Basic Elements of Lean Production
Doing more with less inventory, fewer workers, less space
Just-in-time (JIT)
  smoothing the flow of material to arrive just as it is needed
  “JIT” and “Lean Production” are used interchangeably
Muda
  waste, anything other than that which adds value to product or service

## Slide 8: Waste in Operations
8

## Slide 9: Waste in Operations
9

## Slide 10: Waste in Operations
10

## Slide 11: Basic Elements
Flexible resources
Cellular layouts
Pull system
Kanbans
Small lots
Quick setups
Uniform production levels
Quality at the source
Total productive maintenance
Supplier networks

## Slide 12: Flexible Resources
Multifunctional workers
  perform more than one job
  general-purpose machines perform several basic functions
Cycle time
  time required for the worker to complete one pass through the operations assigned
Takt time
  paces production to match the rate customer demand
12

## Slide 13: Cellular Layouts
Manufacturing cells
  comprised of dissimilar machines brought together to manufacture a family of parts
Cycle time is adjusted to match takt time by changing worker paths
13

## Slide 14: Pull System
Material is pulled through the system when needed
Reversal of traditional push system where material is pushed according to a schedule
Forces cooperation
Prevent over and underproduction
While push systems rely on a predetermined schedule, pull systems rely on customer requests
14

## Slide 15: Kanbans
Card which indicates standard quantity of production
Derived from two-bin inventory system
Maintain discipline of pull production
Authorize production and movement of goods
15

## Slide 16: Sample Kanban
16

## Slide 17: Origin of Kanban
a) Two-bin inventory system b) Kanban inventory system
Reorder
card
Bin 1
Bin 2
Q - R
Kanban
R
R
Q = order quantity
R = reorder point - demand during lead time
17

## Slide 18: Types of Kanban
Production kanban
  authorizes production of goods
Withdrawal kanban
  authorizes movement of goods
Kanban square
  a marked area designated to hold items
Signal kanban
  a triangular kanban used to signal production at the previous workstation
Material kanban
  used to order material in advance of a process
Supplier kanban
  rotates between the factory and suppliers
18

## Slide 19
Product: Just in Time Inventory (JIT) -Kanban
(Collier & Evans, 2007, p. 754; Russell & Taylor, 2011 , pp. 726-730)
19

## Slide 20: Small Lots
Require less space and capital investment
Move processes closer together
Make quality problems easier to detect
Make processes more dependent on each other
20

## Slide 21: Inventory Hides Problems
21

## Slide 22: Less Inventory Exposes Problems
22

## Slide 23: Quick Setups
Internal setup
  Can be performed only when a process is stopped
External setup
  Can be performed in advance
SMED* Principles
  Separate internal setup from external setup
  Convert internal setup to external setup
  Streamline all aspects of setup
  Perform setup activities in parallel or eliminate them entirely
23
* Single Minute Exchange of Die; Quick Changeover

## Slide 24: Techniques for Reducing Setup Time
24

## Slide 25: Techniques for Reducing Setup Time
25

## Slide 26: Techniques for Reducing Setup Time
26

## Slide 27: Uniform Production Levels
Result from smoothing production requirements on final assembly line
Kanban systems can handle +/- 10% demand changes
Reduce variability with more accurate forecasts
Smooth demand across planning horizon
Mixed-model assembly steadies component production
27

## Slide 28: Quality at the Source
Visual control
  makes problems visible
Poka-yokes
  prevent defects from occurring
Kaizen
  a system of continuous improvement; “change for the good of all”
Jidoka
  authority to stop the production line
Andons
  call lights that signal quality problems
Under-capacity scheduling
  leaves time for planning, problem solving, and maintenance
28

## Slide 29: Examples of Visual Control
29

## Slide 30: Examples of Visual Control
30

## Slide 31: 5 Whys
A key part in an effective Kaizen is finding the root cause of a problem and eliminating it
A practice of asking “why?” repeatedly until the underlying cause is identified (usually requiring five questions)
Simple, yet powerful technique for finding the root cause of a problem
31

## Slide 32: 5S Workplace Scan
Seiri
(sort)
Seiton
(set in order)
Seisou
(shine)
5S Scan
Keep only what you need
A place for everything and everything in its place
Cleaning, and looking for ways to keep clean and organized
Goal
Unneeded equipment, tools, furniture; unneeded items on walls, bulletins; items blocking aisles or stacked in corners; unneeded inventory, supplies, parts; safety hazards
Items not in their correct places; correct places not obvious; aisles, workstations, & equipment locations not indicated; items not put away immediately after use
Floors, walls, stairs, equipment, & surfaces not clean; cleaning materials not easily accessible; lines, labels, signs broken or unclean; other cleaning problems
Eliminate or Correct
32

## Slide 33
Seiketsu
(standardize)
Shisuke
(sustain)
5S Scan
Maintaining and monitoring the first three categories
Sticking to the rules
Goal
Necessary information not visible; standards not known; checklists missing; quantities and limits not easily recognizable; items can’t be located within 30 seconds
Number of workers without 5S training; number of daily 5S inspections not performed; number of personal items not stored; number of times job aids not available or up-to-date
Eliminate or Correct
5S Workplace Scan
33

## Slide 34: Benefits of Lean Production
Reduced inventory
Improved quality
Lower costs
Reduced space requirements
Shorter lead time
Increased productivity

## Slide 35: Benefits of Lean Production
Greater flexibility
Better relations with suppliers
Simplified scheduling and control activities
Increased capacity
Better use of human resources
More product variety
35

## Slide 36: Implementing Lean Production
Use lean production to finely tune an operating system
Somewhat different between countries (USA, Aus v Japan)
Lean production is still evolving
Lean production is not for everyone

## Slide 37: Lean Production Problems
Highly variable demand
Large variety of low-volume products
Custom engineered products
Mass production parts
Unexpected changes in demand or supply

## Slide 38: Lean Services
Basic elements of lean production apply equally to services
Most prevalent applications
  lean retailing
  lean banking
  lean health care

## Slide 39
Reduce the cycle time in business processes to Increase the service level
  How?
Services Lean Example: Swedish Hospital
39

## Slide 40: Leaning the Supply Chain
Pull a smooth flow of material through the system
Build a highly collaborative business environment
Adopt the technology to support your system
Consider “near shoring”

## Slide 41
Lean and Six Sigma are natural partners for process improvement
Lean
  Eliminates waste and creates flow
  More continuous improvement
Six Sigma
  Reduces variability and enhances process capabilities
  Requires breakthrough improvements

## Slide 42: In the Lecture we covered:
JIT and Basic Elements of Lean Production
Benefits of Lean Production
Implementing Lean Production
Lean Services
Leaning the Supply Chain
Lean Six Sigma